## Slide 2
Warning
It is totally normal and okay to have moments where you understand nothing in this workshop :v

## Slide 3
01
02
03
04
CONTENTS
Getting started with ESP32
Connecting to WiFi
Getting used to ESP-IDF
TCP/IP sockets

## Slide 4
01
Getting Started with ESP32

## Slide 5
Session’s content:
Introduction to the ESP32 and its’ variants
Comparing ESP32 to Arduino UNO
Getting started with IoT Development Framework
Understand the “blink” example code

## Slide 6
Introduction
ESP32 is a low-cost dual core microcontroller developed by Espressif Systems. It has both WiFi and Bluetooth integrated with various peripherals.

## Slide 7
ESP32 vs Arduino UNO
Specs | ESP32 | Arduino UNO
CPU | Dual Core 160 MHz | Single Core 16MHz
Flash Memory | 4MB | 32KB
SRAM | 520KB | 2KB
GPIOs | 38 | 20
WiFi/Bluetooth | Yes | No
UART (Hardware Serial) | 3 | 1
SPI | 3 | 1
I²C | 2 | 1
Operating Voltage | 3.3V | 5V
Price | 2500DA/ 3.5$ | 2800DA/ 4$

## Slide 8
Other ESPs
ESP8266
ESP32 Wroom
ESP32 Wrover
ESP32-S2
ESP32 PICO D4
ESP32-S3

## Slide 9
Developement boards

## Slide 10
How to program the ESP32
Arduino Framework
Beginner friendly but thats it. Very limited, lacks many features and bad coding mindset (copy-paste)
IoT Dev Framework
Official framework supported by Espressif. Extremely reliable and configurable. Well documented with growing community.
micropython, lua...
Just do not use this.
You do not want a high level language when dealing with microcontrollers.
C/C++ is the way to go with embedded systems.

## Slide 11
Setting up ESP-IDF
Install ESP-IDF with the esp-idf-tools-setup-offline-4.4.exe
Install VSCode
Install the Espressif IDF Extensions in VSCode
F1 or CTRL+Shift+P and search for “Configure ESP-IDF extension”
Choose “Use existing setup”

## Slide 12
Your first ESP-IDF project
F1 or CTRL+Shift+P and search for “new project”
Set project name and directory then choose template
Pick the “blink” example as your project template

## Slide 13
ESP-IDF Project Structure
project configuration files
build system related files
main C file

## Slide 14
ESP-IDF Extension status bar
Port
Target platform
Project directory
Menu Config
Clean project
Build
Flash
Monitor
Build, Flash and Monitor
New IDF terminal

## Slide 15
Arduino Framework vs ESP-IDF
Arduino | ESP-IDF
pinMode(pin, mode) | gpio_set_direction(pin, mode)
digitalWrite(pin, state) | gpio_set_level(pin, state)
Serial.printf() | printf()
delay() | vTaskDelay()
OUTPUT | GPIO_MODE_OUTPUT
INPUT | GPIO_MODE_INPUT

## Slide 16
Thank you

## Slide 17
02
Getting used to ESP-IDF

## Slide 18
Session’s content:
Understand the “Hello World” code example
C Review of basic topics
Learn how to use the ESP-IDF documentation
Use “ESP_LOGx” instead of printf to make log statements